The format of the lfwr*.dat files is:

ASCII

First Line:   Type of Polar Data
Second LIne:  Start time of snapshot in UT (SECT is equivalent to UT)
Third Line:   FFT Size used to calibrate data
Fourth LIne:  Date data generated and by whom
Fifth Line:   Column Headings 1,2,3,4,5,6 where 1,2,3 are the electric
              channels and 4,5,6 are the magnetic channels.  In the case
	      of antenna coordinate system:  Eu,Ev,Ez,Bu,Bv,Bz;
	      dc magnetic field aligned coordinate system:  Experp,Eyperp,
	      Ezpar,Bxperp,Byperp,Bzpar, where Z direction is the direction
	      of the magnetic field, X is the vector in the meridian plane
	      from the center of the earth to the location of the spacecraft,
	      and Y completes the right-handed system, being generally
	      eastward
Lines 6-262   Data.  Each line represents the simultaneous sampling of all
	      6 channels, and all lines are separated by 0.01 seconds.  Thus,
	      if all of the data are good and accounted for, each snapshot
	      will be 2.56 seconds in length.
	      NOTE:  The electric channels are calibrated in mV/m and the
	             magnetics in nT.
		     
Five Line Header in lines 263-267 for next snapshot (~ 28 seconds later)
Lines 268-524 Data

ETC.

NOTE:  Some snapshots have data glitches which we have not attempted to
       remove yet.  You can either average across them, or throw them
       out altogether.  They will be obvious.  Also, there is the
       possibility that some expected snapshots may be missing altogether,
       so it is best to always read the start time of each snapshot in
       the header.