## Slide 1: MARSIS report to SWT
Andy Kopf
On behalf of Roberto Orosei and Jeff Plaut

## Slide 3: Instrument Status

## Slide 4: Operations
Resources to continue MARSIS operations and data processing have been secured until the end of 2021 (1 FTE).
MARSIS operated nominally since the last SWT. No detectable signs of performance degradation or aging.
See presentation at SOWG for details.

## Slide 5: Data Archiving
All MARSIS SS data products acquired up to December 31, 2018, have been delivered to PSA.
An ESA contract for the production of higher-level SS products, “Improved Processing and Science Exploitation of Mars Express MARSIS Radar Data” (Project Leader: Elliot Sefton-Nash) is being assigned to INAF/IRA (R. Orosei) for the production of
  Clutter (surface echo) simulations
  Co-registered radargrams
  TEC estimates
  Raw echo radargrams (flash mode)
  Geometric databases
MARSIS AIS products are also up-to-date on PSA delivery, however:
Most data submitted by the Iowa AIS team since January 2017 are not available yet, including most of those corrected for the timing error: data in the archive are still erroneous. This could become a problem in requesting US funding extensions.

## Slide 6: Science - Subsurface

## Slide 7: Strong radar reflections as evidence for subsurface water
The 2018 paper was based on less than 30 observations acquired using the so-called «superframe» (i.e. high resolution) mode over an area of about 200 km X 200 km.

## Slide 8: An enlarged study area
Discovering more subglacial liquid water bodies has significant implications for the history of water and biologic potential on Mars.
In spite of the low data rate, the first half of 2019 provided an unique opportunity to observe the SPLD with MARSIS.
A campaign of observations covering a much larger area was planned for MARSIS.

## Slide 9: Continuing to look for bright spots
From January to June 2019 MARSIS could acquire 57 new high resolution observations over a 600 km X 600 km area within the SPLD.
This was the last opportunity to acquire such data in favourable conditions (i.e. during the night) for the rest of the mission.
A BIG «thank you» to the MEX Operations Team!
18976 18980 18983 19015 19043 19047 19142 19149 19156 19163 19177 19184 19188 19191 19216 19223 19230 19237 19251 | 19255 19262 19265 19269 19276 19283 19290 19297 19304 19311 19318 19325 19329 19336 19339 19343 19350 19357 19364 | 19371 19378 19385 19392 19396 19399 19403 19410 19431 19438 19459 19466 19470 19477 19480 19484 19491 19498 19505

## Slide 10: Preliminary results
There are indeed several bright areas beyond the one studied in the 2018 paper (look for light blue).
These are weaker reflectors compared to the first one, but still stronger than expected for dry surfaces.
Some are likely to be artifacts, however.
Analysis is ongoing.

## Slide 11: MARSIS will never complete the survey of the SPLD in high resolution mode
There is not enough time nor there are observation opportunities to even approach full coverage of the SPLD within the MEX lifetime.
SHARAD’s frequency is too high to penetrate to the bottom of the SPLD.
Large stretches of the PLD will thus remain Terra Incognita for the detection of potential subglacial water.
The Chinese Huoxing 1 spacecraft, to be launched in Summer 2020, will carry a sounding radar operating at frequencies between those of MARSIS and SHARAD.
Recently, a proposal for a joint European-Chinese study team for the search of subglacial water using radar sounders has been approved by ISSI.

## Slide 12: Science - Ionosphere

## Slide 13: The Solar Wind Flow Alters the Global Structure of Mars’ Ionosphere
When the solar wind collides with Mars, it “pushes” on its induced magnetosphere. This force, called the solar wind dynamic pressure, is routinely monitored by the MAVEN spacecraft.
Left: MARSIS electron density maps as a function of altitude and solar zenith angle for low and high solar wind dynamic pressures. Right: The difference between these two cases as a percentage.
During times of high solar wind dynamic pressure, electron density maps from the MARSIS instrument on Mars Express show that the ionosphere is globally depleted of plasma.
High solar wind dynamic pressures compress the ionosphere on a global scale.
Z. Girazian et al., Geophys. Res. Lett., 2019
Low Pressure
High Pressure
High vs. Low

## Slide 14: Crustal Magnetism Inhibits the Formation of the Ionopause at Mars
Chu et al., Geophys. Res. Lett., 2019
↟ MARSIS ionopause detection. ↡ Locations of the ionopause (grey dots), very few of which are seen over strongest crustal magnetism (red region).
An ionopause is a sharp decrease in the plasma density at the top of the ionosphere, separating the cold, dense ionospheric plasma from the hot, tenuous solar wind plasma.
The MARSIS instrument on the Mars Express spacecraft detects the sharp density gradient by bouncing radio pulses off the ionopause.
Very few ionopauses are detected near the region of strongest crustal magnetism in the southern hemisphere.
The strong crustal magnetism alters the solar wind interaction and prevents the ionopause from forming.

## Slide 15: How do dust storms affect the ionosphere’s peak altitude?
Peak altitude rises as lower atmosphere expands from solar heating of dust
Peak altitude is more variable suggesting increased wave activity coupling the lower and upper atmosphere
Girazian et al., JGR Planets (in press)
Latitude (deg.)
Dust Optical Depth
MARSIS
Coverage
Dust Map
Dust storm

## Slide 16: High-Resolution MARSIS AIS
MARSIS AIS, since the beginning of the mission, has sounded 160 sequential quasi-logarithmic frequencies in ~1.5 sec., and repeated the cycle once every 7.5 sec.
MARSIS was designed to store up to 16 unique frequency tables
By sounding a smaller number of frequencies multiple times, MARSIS can obtain improved frequency resolution at sub-second intervals.
  Example: A set of 20 frequencies sounded 8 times would repeat measurements in 0.2 seconds
Multiple potential targets:
  Ionospheric peak
  Ionopause
  Topside Layers
  “MARSIS Effect” in ASPERA
  Other Ideas Welcome!!!

## Slide 17: High-Resolution MARSIS AIS
Standard MARSIS ionogram, featuring a clear ionospheric trace with a sharp cusp that indicates the observation of the main peak.
Current Frequency Resolution

## Slide 18: High-Resolution MARSIS AIS
A zoomed-in view of the main peak reveals the current density/frequency resolution
Current Frequency Resolution (zoom)
Current
Frequency
Resolution

## Slide 19: High-Resolution MARSIS AIS
An example of a high-frequency resolution mode with 16 sounding frequencies focused near the main peak.
New High Frequency Resolution Mode
Current
Frequency
Resolution
High Frequency
Resolution

## Slide 20
1.1 MARSIS/MEX Sun Elevation Angle Distribution (MTP 205 ÷ MTP 215)
1. PI Science Objectives of Incoming MTPs
MTP205 MTP206 MTP207 MTP208 MTP209 MTP210 MTP211 MTP212 MTP213 MTP214 MTP215
25-1-20 21/2/20 21/3/20 18/4/20 16/5/20 12/6/20 12/7/20 9/8/20 6/9/20 4/10/20 1/11/20 29/11/20
HIGH PRIORITY
LOW PRIORITY
LOW PRIORITY

## Slide 21
1.2 MARSIS/MEX Latitude Distribution (MTP 205 ÷ MTP 215)
HIGH PRIORITY
LOW PRIORITY
LOW PRIORITY
MTP205 MTP206 MTP207 MTP208 MTP209 MTP210 MTP211 MTP212 MTP213 MTP214 MTP215
25-1-20 21/2/20 21/3/20 18/4/20 16/5/20 12/6/20 12/7/20 9/8/20 6/9/20 4/10/20 1/11/20 29/11/20

## Slide 22: Publications since the last SWT
Refereed papers
Arnold et al. 2019. Modeled Subglacial Water Flow Routing Supports Localized Intrusive Heating as a Possible Cause of Basal Melting of Mars' South Polar Ice Cap. JGR Planets 124. DOI 10.1029/2019JE006061
Bernhardt et al. 2019. The banded terrain on northwestern Hellas Planitia: New observations and insights into its possible formation. Icarus 321. DOI 10.1016/j.icarus.2018.11.007
Brouet et al. 2019. A laboratory-based dielectric model for the radar sounding of the martian subsurface. Icarus 321. DOI 10.1016/j.icarus.2018.12.029
Chu et al. 2019. The Effects of Crustal Magnetic Fields and Solar EUV Flux on Ionopause Formation at Mars. GRL 46. DOI 10.1029/2019GL083499
Duru et al. 2019. Electron density profiles in the upper ionosphere of Mars from 11 years of MARSIS data: Variability due to seasons, solar cycle, and crustal magnetic fields. JGR Space Physics 124. DOI 10.1029/2018JA026327
Fallows et al. 2019. Extremely High Plasma Densities in the Mars Ionosphere Associated with Cusp-like Magnetic Fields. JGR Space Physics 124. DOI 10.1029/2019JA026690
Girazian et al. 2019. The Effects of Solar Wind Dynamic Pressure on the Structure of the Topside Ionosphere of Mars. GRL 46. DOI 10.1029/2019GL083643
Nemec et al. 2019. Oblique Reflections of Mars Express MARSIS Radar Signals from Ionospheric Density Structures: Raytracing Analysis. JGR Space Physics 124. DOI 10.1029/2018JE005891
Mohanamanasa et al. 2019. Isolated High-Density Structures in Magnetic Anomaly Regions of the Martian Lower Ionosphere. JGR Space Physics 124. DOI 10.1029/2018JA026400

## Slide 23: Publications since the last SWT (2)
Refereed papers
Piazzo et al. 2019. Signal enhancement for planetary radar sounders. Electronics Letters 55. DOI 10.1049/el.2018.7284
Rao et al. Enhanced Ionization in Magnetic Anomaly Regions of the Martian Lower Ionosphere Associated With Dust Storms. JGR Space Physics 124. DOI 10.1029/2018JA026283
Sanchez-Cano et al. 2019. Origin of the Extended Mars Radar Blackout of September 2017. JGR Space Physics 124. DOI 10.1029/2018JA026403
Vázquez-Poletti et al. 2018. Serverless Computing: From Planet Mars to the Cloud. Computing in Science & Engineering 20, 10.1109/MCSE.2018.2875315
Submitted papers
Conroy et al. A new method for determining the total electron content in Mars’ ionosphere based on Mars Express MARSIS data. Submitted to PSS.
Girazian et al. Variations in the ionospheric peak altitude at Mars in response to dust storms: 13 years of observations from the Mars Express radar sounder. Submitted to JGR Space Physics.
Lauro et al. Liquid water detection under the Polar Layered Deposits of Mars: A rigorous methodological approach. Submitted to TGRS.
Sanchez-Cano et al. Mars’ ionospheric interaction with comet C/2013 A1 Siding-Spring’s coma at their closest approach as seen by Mars Express. Submitted to JGR Space Physics.
Voschepynets et al. Observations of sounder accelerated electrons by Mars Express. Submitted to JGR Space Physics.