## Slide 1
Cluster extension 2017-2018, 2019-2020 Science
C. Philippe Escoubet
Project Scientist on behalf of
Cluster Science Working Team
13/10/2016

## Slide 2: Cluster Science
Cluster science performance
Cluster confirmation that science objectives planned in 2017-2018 can be achieved
Cluster new science objectives for 2019-2020

## Slide 3: Cluster
Four identical spacecraft
44 instruments with 76 sensors
Measurements:
  Ions, e- (2,5,6)
  Magnetic field (4)
  Electric field (3,8)
  Electromagnetic waves (7,9,10,11)
  Spacecraft potential control (1)

## Slide 4: Cluster Science
Cluster science performance
Cluster confirmation that science objectives planned in 2017-2018 can be achieved
Cluster new science objectives for 2019-2020

## Slide 5: Cluster refereed publications 1
Chart: Cluster and Double Star refereed publications 31 August 2016 Total: 2394 (+ 334 in 2 years)
| Before 2001 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Overall | 60 | 99 | 121 | 186 | 314 | 500 | 648 | 777 | 976 | 1154 | 1352 | 1587 | 1776 | 1949 | 2108 | 2287 | 2328
Cluster | 60 | 99 | 121 | 186 | 314 | 500 | 648 | 777 | 976 | 1154 | 1352 | 1587 | 1776 | 1949 | 2108 | 2287 | 2328
Double Star | 0 | 1 | 1 | 1 | 2 | 29 | 36 | 48 | 88 | 99 | 114 | 125 | 131 | 135 | 140 | 144 | 145
August 2016

## Slide 6: Cluster refereed publications 2
Journals | 
Nature/Science | 26
JGR | 818
GRL | 234
Annales Geophysicae | 516
Physics of Plasmas | 61
Physical Review Letters | 69
Astrophysical Journal (incl. Lett.) | 59
Others | 611
Total | 2394
Chart: 
| USA | China | Europe | Rest of the World
 | 25 | 12 | 51.6 | 12.4
Europe
50%
China
12%
USA
25%
Rest of the World
13%

## Slide 7: Cluster inter-spacecraft distances
41 constellation manoeuvres
2nd Guest Investigator (GI) operations completed
Large distances (27000 km) repeated in Spring 2016
Smallest distance achieved in 2016: 3 km
New tetrahedron in 2016-2017
3 km

## Slide 8: Cluster Science
Cluster science performance
Cluster confirmation that science objectives planned in 2017-2018 can be achieved
Cluster new science objectives for 2019-2020

## Slide 9: Scientific performance for 2017 and 2018
to characterise the jet braking region with Cluster at multi-scales
  Orbit is as expected and instruments are working nominally (mission extension review)
to determine the extent of the polar cusp in longitude and investigate its dawn dusk asymmetries
  Orbit is as expected and instruments are working nominally
to study the magnetosphere-ionosphere coupling together with Swarm with 60-90 deg. orbits
  Cluster and Swarm working as expected. Swarm collaborations initiated. Swarm nominal mission up to May 2018 which is enough for investigation
to investigate the macro and micro physics scales of the magnetosphere simultaneously using THEMIS, Van Allen Probes and MMS constellation missions
  THEMIS, Van Allen Probes collaborations initiated. MMS launched as planned in March 2015. THEMIS-Cluster workshop in Nov. 2016 (MMS invited but it was too early for them)
Notes: Many teams in European labs working on both MMS and Cluster data.

## Slide 10: Cluster Science
Cluster science performance
Cluster confirmation that science objectives planned in 2017-2018 can be achieved
Cluster new science objectives for 2019-2020

## Slide 11: Cluster Science Objectives for 2019-2020
To characterise chorus waves at both low and high-latitude with 3km inter-spacecraft distance
To investigate bow shock/magnetosheath/magnetopause physics with local solar wind monitor
To investigate evolution of Kelvin–Helmholtz waves on the flank of the magnetosphere
To open a call for young scientists to perform Cluster science operations (spacecraft separation+instrument modes) for 3 months.

## Slide 12: Cluster Science Objectives for 2019-2020
To characterise chorus waves at both low and high latitude with 3km inter-spacecraft distance
To investigate bow shock/magnetosheath/magnetopause physics with local solar wind monitor
to investigate evolution of Kelvin–Helmholtz waves on the flank of the magnetosphere
To open a call for young scientists to perform Cluster science operations (spacecraft separation+instrument modes) for 3 months.

## Slide 13
[Inan al., 2004]
Chorus are electromagnetic waves at audible frequencies naturally generated in space close to the magnetic equator or magnetic minimum.
Play an important role in the local acceleration of electrons to relativistic energies in the outer radiation belt.
Chorus observations frequency shift
C1
C2
Notes: The first simultaneous measurements of discrete chorus emissions on multiple spacecraft, realized in the context of the Cluster mission, revealed a rather unexpected frequency difference of around 1 kHz between nearly identical discrete elements observed on different spacecraft [Gurnett et al., 2001]. This frequency difference is interpreted herein as a natural outcome of the dependence of the whistler-mode refractive index on the wave normal angle between the wave vector k and the static magnetic field B0 and the rapid motion of highly localized source region(s) of chorus of 400 km to 1700 km in extent along the field line, but only less than 100 km transverse to the magnetic field, and moving at speeds of 20,000 km/s to 25,000 km/s. Wave packets emanating from the localized regions propagate to two spacecraft at different wave normal angles, and are observed at different frequencies due to the differential Doppler shift between the two spacecraft. These differences in frequency, as well as the different times of arrival of the similar emissions at the different spacecraft, provide a unique opportunity to estimate the source characteristics, using a model involving rapidly moving sources traveling at speeds comparable to the parallel resonant velocity of counterstreaming electrons moving along the Earth's magnetic field lines. We report the determination of chorus emission source region motion for two different cases observed during 2000-2001, where these differences in frequency were readily observable due to the relatively large separation of the Cluster spacecraft. We also report a case in 2002 where the spacecraft separations were smaller, so that these frequency differences were not as evident but nevertheless measurable. In general, our results provide the first experimental evidence that the sources that generate the discrete chorus emissions are in rapid motion.

## Slide 14
[Inan al., 2004]
Chorus are electromagnetic waves at audible frequencies naturally generated in space close to the magnetic equator or magnetic minimum.
Play an important role in the local acceleration of electrons to relativistic energies in the outer radiation belt.
Chorus observations frequency shift
C1
C2
1 kHz
shift
Notes: The first simultaneous measurements of discrete chorus emissions on multiple spacecraft, realized in the context of the Cluster mission, revealed a rather unexpected frequency difference of around 1 kHz between nearly identical discrete elements observed on different spacecraft [Gurnett et al., 2001]. This frequency difference is interpreted herein as a natural outcome of the dependence of the whistler-mode refractive index on the wave normal angle between the wave vector k and the static magnetic field B0 and the rapid motion of highly localized source region(s) of chorus of 400 km to 1700 km in extent along the field line, but only less than 100 km transverse to the magnetic field, and moving at speeds of 20,000 km/s to 25,000 km/s. Wave packets emanating from the localized regions propagate to two spacecraft at different wave normal angles, and are observed at different frequencies due to the differential Doppler shift between the two spacecraft. These differences in frequency, as well as the different times of arrival of the similar emissions at the different spacecraft, provide a unique opportunity to estimate the source characteristics, using a model involving rapidly moving sources traveling at speeds comparable to the parallel resonant velocity of counterstreaming electrons moving along the Earth's magnetic field lines. We report the determination of chorus emission source region motion for two different cases observed during 2000-2001, where these differences in frequency were readily observable due to the relatively large separation of the Cluster spacecraft. We also report a case in 2002 where the spacecraft separations were smaller, so that these frequency differences were not as evident but nevertheless measurable. In general, our results provide the first experimental evidence that the sources that generate the discrete chorus emissions are in rapid motion.

## Slide 15
[Inan al., 2004]
Chorus observations frequency shift: under debate
Propagation vs B + high speed of source (Inan et al., 2004) or
Fixed source with frequency variations of directional emission pattern (Chum et al., 2007)
Notes: The first simultaneous measurements of discrete chorus emissions on multiple spacecraft, realized in the context of the Cluster mission, revealed a rather unexpected frequency difference of around 1 kHz between nearly identical discrete elements observed on different spacecraft [Gurnett et al., , 2001]. This frequency difference is interpreted herein as a natural outcome of the dependence of the whistler-mode refractive index on the wave normal angle between the wave vector k and the static magnetic field B0 and the rapid motion of highly localized source region(s) of chorus of 400 km to 1700 km in extent along the field line, but only less than 100 km transverse to the magnetic field, and moving at speeds of 20,000 km/s to 25,000 km/s. Wave packets emanating from the localized regions propagate to two spacecraft at different wave normal angles, and are observed at different frequencies due to the differential Doppler shift between the two spacecraft. These differences in frequency, as well as the different times of arrival of the similar emissions at the different spacecraft, provide a unique opportunity to estimate the source characteristics, using a model involving rapidly moving sources traveling at speeds comparable to the parallel resonant velocity of counterstreaming electrons moving along the Earth's magnetic field lines. We report the determination of chorus emission source region motion for two different cases observed during 2000-2001, where these differences in frequency were readily observable due to the relatively large separation of the Cluster spacecraft. We also report a case in 2002 where the spacecraft separations were smaller, so that these frequency differences were not as evident but nevertheless measurable. In general, our results provide the first experimental evidence that the sources that generate the discrete chorus emissions are in rapid motion.

## Slide 16
Tsurutani and Smith, JGR 1977
High-latitude
Chorus
Equatorial chorus
Chorus emissions at 3 km inter-spacecraft distance
High-latitude chorus:
  locally generated (Vaivads et al., 2007) or
  propagating from equatorial region (Menietti et al., 2009)
Cluster: only mission able to study high-latitude chorus with polar orbit
Chorus at high-latitude: local or remote generation

## Slide 17
Low and high latitude chorus quasi-simultaneously in October 2019
Low latitude chorus (3h later)
Cluster
High latitude chorus
Current chorus observations 2019
Notes: We may also think if laging one s/c by a few hours would allow to observe both low and high latitude at the same time. This could be combine with the large manoeuvre for local solar wind monitor

## Slide 18
Low and high latitude chorus quasi-simultaneously in October 2019
Low latitude chorus (3h later)
Cluster
High latitude chorus
Current chorus observations 2019: C1 drift by 3h
Notes: We may also think if laging one s/c by a few hours would allow to observe both low and high latitude at the same time. This could be combine with the large manoeuvre for local solar wind monitor

## Slide 19: Cluster Science Objectives for 2019-2020
To characterise chorus waves at both low and high latitude with 3km inter-spacecraft distance
To investigate bow shock/magnetosheath/magnetopause physics with local solar wind monitor
to investigate evolution of Kelvin–Helmholtz waves on the flank of the magnetosphere
To open a call for young scientists to perform Cluster science operations (spacecraft separation+instrument modes) for 3 months.

## Slide 20: Cluster measurements of dayside plasma boundaries and structures
Bow
shock
Magnetopause
Sun
Cluster
Solar
wind
Magnetosheath structures:
Hot flow anomalies
High-speed jets

## Slide 21: Solar wind “classical” L1 monitor
30min-1h30
Propagation time
Solar
wind
10 Re
ACE/SOHO/Wind
L1
220 Re
=> L1 too far away for structures in dayside boundaries
(Case and Wild, 2012)

## Slide 22: C1 as “local” solar wind monitor: lag other s/c by 8h
C1
C2,C3,C4
Use one of the Cluster spacecraft as local solar wind monitor
Local solar wind monitor for extended period of time
Would take up 3-6 months to drift C1 to that position

## Slide 23: Cluster Science Objectives for 2019-2020
To characterise chorus waves at both low and high latitude with 3km inter-spacecraft distance
To investigate bow shock/magnetosheath/magnetopause physics with local solar wind monitor
to investigate evolution of Kelvin–Helmholtz waves on the flank of the magnetosphere
To open a call for young scientists to perform Cluster science operations (spacecraft separation+instrument modes) for 3 months.

## Slide 24: Kelvin-Helmholtz waves observed by Cluster
Vortex
Cluster
H. Hasegawa et al., 2004)
Kelvin-Helmholtz waves rolling-up
Notes: Les vents solaires, plasma emis continuellement par le soleil, peut sous certaines condition creer de gigantesques vortex a la surface externe de la magnetosphere
C’est analoque au vent qui donne naissance aux vagues a la surface de l’ocean. Ce qu’on voit avec Cluster, grace a ses observations en 3D, c’est que les vagues s’enroulent sur elles memes pour creer des vortex.
C’est un processus tres important car il permettrai au particules du vent solaire d’entrer dans la magnetosphere. Les particules du vent solaire peuvent produires les aurores polaires mais aussi avoir des effets dramatiques sur la vie de tous les jours (communications, anomalies ou destructions satellites, lignes electriques en sur-tension dans les pays Nordqiues.

## Slide 25: Ideal configuration of Cluster-MMS to study K-H waves evolution
Evolution of Cluster and MMS orbits approach them in 2019
Cluster and MMS will be skimming the magnetopause
MMS high resolution small scales and Cluster multi-scales
SWARM will investigate effect of K-H waves in the polar cap
=> evolution of K-H waves as they propagate downstream
=> reconnection inside vortex with 4 points measurements
MMS
(4 s/c)
Cluster
(4 s/c)
THEMIS
(3 s/c)
SWARM
(3 sc)
Sun
Notes: MMS and Swarm not yet extended but likely to happen.

## Slide 26: Cluster Science Objectives for 2019-2020
To characterise chorus waves at both low and high latitude with 3km inter-spacecraft distance
To investigate bow shock/magnetosheath/magnetopause physics with local solar wind monitor
to investigate evolution of Kelvin–Helmholtz waves on the flank of the magnetosphere
To open a call for young scientists to perform Cluster science operations (spacecraft separation+instrument modes) for 3 months.

## Slide 27: Science Operations Planning by Young scientists 1/2
Train young European scientists: play the role as PI of an ESA space mission.
Create a network of young European space scientists (publish joint papers).
Science planning using fresh eyes and new ideas.
Outreach (web stories)

## Slide 28: Science Operations Planning by Young scientists 2/2
AO for PhDs-PhDs+4 years
Cover 3 month Cluster planning (s/c config + instr. modes)
Young scientists invited to two SOWGs:
  1st SOWG: 1 day training on mission+instruments + participation to SOWG
  2nd SOWG: young scientists decides s/c config + instr.
Scientific proposal by young scientists: select 5-10 scientists and only the best proposal to be implemented

## Slide 29: Why is Cluster unique?
  Polar orbit: Cluster
    - Equatorial orbit: Geotail, THEMIS, Van Allen Probes, MMS
  Constellation: ion scale tetrahedron and multi-scale (e-/ion, ion/fluid)
  Most sensitive search coil magnetometer (turbulence)
  Unique active plasma sounder (absolute local density)
Latest Tsyganenko model
Data used (Cluster in green) 1995-2012
Cluster
Geotail
Polar
THEMIS A,D,E
THEMIS B,C
[Tsyganenko 2014]

## Slide 30: Cluster Science Archive
Contains all high-resolution data from Cluster instruments
Total number of users over 1900
Average monthly active IP number around 180
Average monthly download rate of 2 TB (10 TB peak)
Calibration effort:
  2 cross-calibration meetings/year
  1 annual review
first dedicated book on the Cluster archive was published in 2010 and consisted of more than 30 refereed papers (11632 chapters downloaded, 70% in 2014-2015)
Notes: A call is done synchronously to the server

## Slide 31: Summary and conclusion
Cluster continues to make discoveries and has a high scientific output thanks its unique orbit, the capabilities to change the spacecraft distances and the fast access to all data
Extension 2017-2018:
  All four science objectives presented in 2014 can be achieved
Extension 2019-2020 new science objectives:
  To characterise chorus waves at both low and high latitude with 3km inter-spacecraft distance
  To investigate bow shock/magnetosheath/magnetopause physics with local solar wind monitor
  to investigate evolution of Kelvin–Helmholtz waves on the flank of the magnetosphere
  To open a call for young scientists to perform Cluster science operations (spacecraft separation + instrument modes) for 3 months.