Plasmaspheric Density StructuresR R Anderson (The University of Iowa, Department of Physics and Astronomy,   Iowa City, IA  52242, USA; 319-335-1924; e-mail: roger-r-anderson@uiowa.edu);  M B Moldwin, H Rassoul, and P Douglas (All at Florida Institute of   Technology, Department of Physics and Space Science, 150 West University   Blvd., Melbourne, FL 32901-6975, USA; 407-674-7208, e-mail:   moldwin@pss.fit.edu), D L Carpenter (Space Telecommunications And   Radioscience Laboratory, Department of Electrical Engineering/SEL, 319   Durand Building, Stanford University, Stanford CA 94305-4055, USA;   650-723-3585; e-mail: dlc@nova.stanford.edu), W Calvert(University of   Massachusetts Lowell,600 Suffolk Street,Lowell MA 01854, USA; 319-337-6368;   e-mail: calvert@fyiowa.info.net); and M F Thomsen (Space and Atmospheric   Sciences, Los Alamos National Laboratory, MS D466, Los Alamos, NM 87545,   USA; 505-667-1210;e-mail: mthomsen@lanl.gov)The International Sun Earth Explorer (ISEE-1) Plasma Wave Investigation (PWI) provided measurements of plasma density in the Earth's plasmasphere during the perigee portion of its 30 degree inclination 57 hour orbit for nearly ten years from October 1977 to September 1987.  The Combined Release and Radiation Effects Satellite (CRRES) Plasma Wave Experiment (PWE) provided measurements of plasma density in the Earth's near-equatorial and low-latitude plasmasphere and magnetosphere from 350 km altitude out to 6.3 Re geocentric for nearly 15 months beginning in August 1990 through October 1991.  The CRRES orbital period of nine hours and 50 minutes and the 18 degree inclination provided nearly 2000 passes (one outbound and one inbound for each orbit) through the inner magnetosphere.  The POLAR PWI provided plasma density measurements in its 2 Re by 9 Re 18 hour polar orbit for about 18 months from late-March 1996 through mid-September 1997.  The plasma wave measurements from these experiments yielded the total electron density independent of spacecraft charging.  Within the plasmasphere, emissions at the upper hybrid resonance frequency (Fuhr) were detected from which, along with the knowledge of the local electron cyclotron frequency (Fce), the plasma frequency (Fp) could be computed: Fp = SQRT (Fuhr**2 - Fce**2).  In the outer magnetosphere the density was determined from the lower cutoff of the continuum radiation at the local plasma frequency:Ne(e/cc) = (Fp(kHz)/8.98)**2.  As the geomagnetic conditions changed, much structure and variability were frequently observed in the plasmasphere and magnetosphere especially near the plasmapause.  These included multiple plasmapauses and "detached" plasma regions.  During geomagnetically active times multiple plasmapauses were often observed.  The location of the plasmapause and the density profiles within the plasmasphere determined by the CRRES and POLAR measurements as a function of local time and geomagnetic activity will be compared with ISEE results acquired over a ten-year period and with other satellite and ground measurements.  We will also compare these with the azimuthal density structure measured by the Magnetospheric Plasma Analyzer (MPA) instruments on multiple LANL geosynchronous satellites in order to study plasma dynamics in the magnetosphere as a function of geomagnetic activity, ring current intensity, and substorm activity.  Evolving models of the depletion and filling of flux tubes either resulting from or tested by these observations will be examined.  Ducted auroral kilometric radiation, auroral myriametric radiation, trapped terrestrial continuum radiation, and other weaves associated with the density structures will also be discussed.